Genie

Hand Shower (Matt Black)

FFASS505-000610BT0

FEATURES

- Easy for consumer to know if nozzles are blocked through transparent faceplate and back part.

- Easy to open and assemble the back part through maintenance key

- Better integrated design through dual injection

- w/ shower holder

- w/ 1.5 M PVC shower hose

- G1/2” inlet thread

SPECIFICATIONS

With 2.5 GPM flow regulator

Flow rate ≥4.0L/min at 0.05 Mpa

Height of spray spouting vertically ≥300mm at 0.1Mpa

Temperature drop: less than 3℃.

FINISHES AVAILABILITY

Matt Black

AWARDS WON

Reddot design

SHIPPING WEIGHT

Product gross weight: 0.4kg / set

Product net weight:  0.57kg / set

STANDARDS CRITERIA

TIS 2066-2552

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice, we assume no liability for the use of obsolete dimensions.

# Text boxes

DIMENSIONAL DRAWING