Genie

Hand shower

FEATURES

- Enhance water pressure for a full, robust shower experience that’s gentle on your skin

- Transparent face plate allows consumers to know if nozzles are blocked

- Easy to open back cover to wipe off any dirt and/or grime build up

- Maintenance key included to open back cover

- Integrated design through dual injection production technique

SPECIFICATIONS

With 2.5 GPM Neoperl regulator

0.10MPa，4.2 L/min≤Q≤8L/min

0.30MPa，Q≤9L/min

Temperature drop : less than 3℃.

Under 0.1Mpa，height of spray spouting vertically≥280mm

Flow at low pressure: Under 0.05Mpa，flow rate≥4.0L/Min

G1/2 thread

Three colours to select from:

Aquamarine, Petal Pink, Steel Gray

STANDARDS CRITERIA

AS WI10.0406

GB/T 23447-2009

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice, we assume no liability for the use of obsolete dimensions.

# Text boxes

DIMENSIONAL DRAWING