Easyflo

Push Basin Mono

FFAST823-109440BP0

FEATURES

- Switch button, enjoying an convenient & easy operation

- High quality cartridge for longer usage

- Zinc die casting chromed body

- Plastic inner water-way

- Reducing metallic pollutant precipitation

- W/ neoperl aerator

- W/o pop-up drain

- W/ normal Package

SPECIFICATIONS

Deck-mounted

Cartridge: 500,000 times for life cycle

Flow rate @0.1MPa: 3.87 L/min for spout

Spout Reach: 100 mm

Spout Height:  81 mm

FINISHES AVAILABILITY

Matt Black

AWARDS WON

N/A

SHIPPING WEIGHT

Product gross weight:  0.7kg

Product net weight:      0.580kg

STANDARDS CRITERIA

GB-18145

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice, we assume no liability for the use of obsolete dimensions.

Rev.: D0

# Text boxes

DIMENSIONAL DRAWING