Sensor Foam Dispenser-AC/DC

FFAS8102-AD0500BF0

FEATURES

- Brass body

- Foam soap

- Sensor distance:9±1cm

- AC 100-240V or DC 6V(4pcs D size battery)

- standby energy consumption <2W; working energy consumption <4W

- soap viscosity range:1-20cp

- Soap volume ≤ 2mLPF

SPECIFICATIONS

Sensor installed at the spout

Faucet  Reach: 136mm

Faucet  Height:  171mm

FINISHES AVAILABILITY

Chrome (- CP)

AWARDS WON

N/A

SHIPPING WEIGHT

Product net  weight:  2.3kg/set

Product gross  weight:2.35 kg/set

STANDARDS CRITERIA

CJ194-2014

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice, we assume no liability for the use of obsolete dimensions.

# Text boxes

DIMENSIONAL DRAWING