Neo Modern

Concealed Bath & Shower Mixer

FFAS0721-609500BF0

FEATURES

- A grade DR brass, strong and durable

- High quality ceramic valve for longer usage

- Ceramic cartridge tested = 500,000 times

- 2-way diverter for spout and shower head

- Without shower kits

- With normal packaging

- Flow rate @ 0.1MPa: 12 L/min for spout

- Flow rate @ 0.1MPa: 12 L/min for shower outlet

SPECIFICATIONS

Concealed bath & shower mixer valve

In-wall installation

Lever handle (cold & hot)

FINISHES AVAILABILITY

Chrome (- CP)

AWARDS WON

N/A

SHIPPING WEIGHT

Product gross weight: 1.8 kg/set

Product net weight:  1.5 kg/set

STANDARDS CRITERIA

GB 18145-2014

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice, we assume no liability for the use of obsolete dimensions.

# Text boxes

DIMENSIONAL DRAWING