Self-closing Faucet

Self-closing Faucet

FFAS4609-101500BF0

FEATURES

- A grade brass body, strong and durable

- Self-closing cartridge

- Zinc hand

- w/ neoperl aerator

- w/ brass pop-up drain

- w/ normal packaging

- Water volume per cycle @ 0.1MPa: 0.31LPF

- Water volume per cycle @ 0.2MPa: 0.31LPF

- Water volume per cycle @ 0.3MPa: 0.32LPF

SPECIFICATIONS

Deck-mounted Installation: lever handle (cold)

Spout Reach: 97 mm

Spout Height: 60 mm

FINISHES AVAILABILITY

Chrome (- CP)

AWARDS WON

N/A

SHIPPING WEIGHT

Product gross weight:  1.6 kg / set

Product net weight:  1.45 kg / set

STANDARDS CRITERIA

TIS 1377-2008

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice, we assume no liability for the use of obsolete dimensions.

# Text boxes

DIMENSIONAL DRAWING