SenseFlow

Concealed sensor urinal

FFAS8604-005500BC0

FEATURES

- A grade brass, strong and durable

- Infrared Sensor

- Alkaline Battery AA(4PCS)

- With normal packaging

- With a flush when 24 hours with no detection

- 3LPF flush volume (Dynamic Pressure1 bar)

SPECIFICATIONS

Sensor  urinal

panel  Reach: 150mm

panel  Height:  130mm

FINISHES AVAILABILITY

Chrome (- CP)

AWARDS WON

N/A

SHIPPING WEIGHT

Product weight:  1.35 kg/set

Product gross  weight:  1.5 kg/set

STANDARDS CRITERIA

TIS 2067-2552

GB 18145-2014

LEED

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice, we assume no liability for the use of obsolete dimensions.

# Text boxes

DIMENSIONAL DRAWING