Loven

Exposed Shower Mixer

FFAS1M12-709500BC0

FEATURES

- Cool touch design: zinc die casting body + plastic water way

- Lixil 35mm High quality ceramic valve for longer usage

- Ceramic cartridge tested = 500,000 times

- Without shower kits

- With normal packaging

- Flow rate @ 0.1MPa: 13 L/min for shower outlet

SPECIFICATIONS

Exposed Shower Mixer Faucet

2-Hole Installation: lever handle (cold & hot)

FINISHES AVAILABILITY

Chrome (- CP)

AWARDS WON

N/A

SHIPPING WEIGHT

Product gross weight:  1.04kg /set

Product net weight:  1.18kg /set

STANDARDS CRITERIA

GB 18145-2014

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice, we assume no liability for the use of obsolete dimensions.

# Text boxes

DIMENSIONAL DRAWING