TemptaCion Auto Temperature Shower System (3-way)

FFAS4952-601500BC0

FEATURES

- German thermostatic cartridge

- Cool touch design, no risk of scalding on the body

- High quality THM valve for utmost precision, with Anti-scald button

- Diverter with shut off function for longer usage

- Diverter with shut off function tested = 300,000 times

- Inline diverter for head shower and hand shower   tested = 100,000 times

- Neoperl hidden flow regulator

- 5-functions hand shower

- The diameter of the head shower is 200 mm

- PVC Silver twist-free shower hose

- With easy glide shower holder

- With normal packaging

- Flow rate @ 0.1MPa: 4.6L/M for hand shower

- Flow rate @ 0.1MPa: 4.5 L/M for shower head

- Flow rate @ 0.1MPa: 15.2 L/M for Spout

SPECIFICATIONS

Exposed THM mixed

Two handles (THM handle & Shut off handle)

Inline diverter to switch water to hand shower and

head shower

FINISHES AVAILABILITY

Chrome (- CP)

AWARDS WON

N/A

SHIPPING    WEIGHT

Product gross weight:  8.06kg/set

Product net weight:      6.26kg/set

STANDARDS CRITERIA

QB 2806-2017

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice, we assume no liability for the use of obsolete dimensions.

Rev.: D0

# Text boxes

DIMENSIONAL DRAWING