DuoSTIX

Hand Shower

FFASS507-000090BF0 (Glossy White)

FFASS507-000440BF0 (Matte Black)

Glossy White                Matte Black

FEATURES

- ABS Plastic body, chrome plating for durable finish

- Two color option for the faceplate: Glossy White and Matte Black

- Two functions: rain and jet spray

- Easy to take the cap off for jet spray function

- DIY color box packaging

- Flow rate @ 0.1MPa: 7 L/min

@ 0.3MPa: 9 L/min

SPECIFICATIONS

Hand shower with 2.5 GPM Neoperl regulator

flow rate at 0.10MPa: ≤8L/min

flow rate at 0.30MPa: ≤9.5L/min

G1/2 thread for inlet

Twi kinds of color for faceplate:

Glossy White, Matte Black

FINISHES AVAILABILITY

Chrome (CP)

AWARDS WON

NA

SHIPPING WEIGHT

Product gross weight: 0.16 Kg/set

Product net weight: 0.12 Kg/set

STANDARDS CRITERIA

TIS 2066-2552

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice, we assume no liability for the use of obsolete dimensions.

Rev.: D/0

# Text boxes

DIMENSIONAL DRAWING