DuoSTIX

Hygiene Spray with Hose and Holder

FFASTS28-000090BF0 (Chrome & Glossy White)

FFASTS28-000440BF0 (Chrome & Matte Black)

FFASTS28-000091BF0 (Glossy White)

FEATURES

- ABS plastic body, chrome plating for durable finish

- Three color options:

Chrome &Glossy White, Chrome & Matte Black, Glossy White

- Two functions: spray and jet spray

- W/ anti-microbial material for Glossy White body

- Easy to take the cap off for jet spray function

- 100,000 life cycles for on/off

- With 1.2M flexible hose

- With fixed angle shower holder

- DIY color box packaging

- Flow rate @ 0.1MPa: 5 L/min

SPECIFICATIONS

Hygiene Spray

flow rate at 0.10MPa: ≤6L/min

G1/2 thread for inlet

Three color options:

Chrome & Glossy White, Chrome &Matte Black, Glossy White

FINISHES AVAILABILITY

Chrome (CP)

AWARDS WON

NA

SHIPPING WEIGHT

Product gross weight: 0.45 Kg/set

Product net weight: 0.35 Kg/set

STANDARDS CRITERIA

TIS 1497-2005

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice, we assume no liability for the use of obsolete dimensions.

Rev.: D/0

# Text boxes

Chrome & Matte Black

Chrome & Glossy White

Glossy White WhiteWhhiwwwwftggtttWwffasrrrWhiWWhite

DIMENSIONAL DRAWING